System Structure
Service-Aware Part
of Instrument SW
Instrument Flight SW (IFSW)
Application Software
Out-Going Reports &
Incoming Commands
Incoming Reports &
Out-Going Commands
Basic Software
Boot Software
Connection to OBC
(1553, PUS-Based)
Connection to SEM
(SpW, PUS-Based)
DPU Processor
Service-Aware Part
of Instrument SW
Instrument SW
Application Software
Basic Software
Connection
to OBC
Connection
to SEM
Boot Software
DPU Processor
SEM Data
SEM Cmd
Cycl. Exec.
Cmd Packet
Rep Packet
Time

---
Service-Aware Part
of Instrument SW
Instrument Flight SW (IFSW)
Application Software
Out-Going Reports &
Incoming Commands
Basic Software
Boot Software
DPU Processor
Service Data Unit
Science Data Buffer
Collection Algorithm
To Ground via
Service 13 only when
SEM Operational SM is
In SCIENCE or CCD_FULL
From SEM via
SEM Operational SM
when SM is in SCIENCE
Or CCD_FULL
SDB
SDB
SDB
SDU2
Toggle buffers which are switched
when a new CCD Frame
is received from the SEM

---
Actions performed by
commands on application
Application-Specific Components
Data loaded by
application into reports
PUS Extension
of CORDET FW
InCmd
OutReport
Management of
command and report flow
CORDET Framework
InStream
OutStream
Interface to MW
and OS
Raw TC Packets
Raw TM Packets

---
Cordet Editor
Cordet Editor
Definition of
Spec. Item
Categories
Definition of
Generators
Editor Meta-Model
Editor Model
Instantiated Editor
Population of
Database through
Editor interface
Editor Model
Model Instance

---
Hardware-Dependent
Modules
Req.
p_link
p_link
Service
Packet
p_link
s_link (from Packet)
Adapt.
Point
Application
Cmd/Rep
s_link
p_link
p_link
s_link
Enum
Type
Enum
Value
Derived
Packet
p_link
p_link
p_link
s_link
Data
Item Type
Data
Item
Packet
Param.
p_link

---
TS defines
inputs
TS evaluates
outputs
Test Sequence
Stub(s)
Config. Data
Module(s)
Under Test
Outputs
Inputs
EGSE
TS defines
inputs
TS evaluates
outputs
General-Purpose Computer
Test Sequence
Stub(s)
Config. Data
Module(s)
Under Test
Inputs
Outputs
DPU B/B
Input Link to
DPU is still TBD
Output Link from
DPU is still TBD

---
TC to DPU
TM from DPU
EGSE
TM/TC Link
Electrical Stimulation
Test Sequence
Stub(s)
Config. Data
Module(s)
Under Test
IFSW
SEM B/B
DPU B/B
OBC Sim.
Spacewire
TBD Link

---
TC to DPU & TM
from SEM and DPU
EGSE
TM/TC Link
Electrical Stimulation
Test Sequence
Config. Data
IFSW
IFSW
SEM EM
DPU TBD
OBC Sim.
Spacewire
TBD Link

---
TC to DPU & TM
from SEM and DPU
EGSE
TM/TC Link
Optical/Electrical Stimulation
Test Sequence
Config. Data
IFSW
IFSW
FPM
SEM FM
BEE FM
OBC TBD
Spacewire
TBD Link
DPU+PSU